## Slide 1: Energy datapalooza Showcase Demo: Green Button Rate Integration Tool
Marty Burns | David Wollman | Erich Gunther
Hypertek, Inc. | NIST | EnerNex

## Slide 2: An overnight success … years in the making
OpenADE (Open Automated Data Exchange)
  Early requirements effort for securely sharing energy information with 3rd parties
NIST SGIP Priority Action Plans 10 & 20
  Accelerates issue resolution and consensus development
OpenADE/SGIP inputs to NAESB standard REQ21
  Energy Services Provider Interface (ESPI)
  Privacy: REQ22 Third Party Access to Smart-Meter-based Information
Flexible file format basis for Green Button
  initial implementation use a subset of ESPI and energy usage information.
Notes: Consensus - emerges around an industry standard North American Energy Standards Board (NAESB) Energy Usage Information (PAP10) completed

## Slide 3: Green Button Enabling Vision
Overall Usage
History of Usage
Cost of Usage

## Slide 4: Green Button Download My Data
Source:
Common-sense idea that electricity customers should be able to download their own energy usage information in a consumer- and computer-friendly format.

## Slide 5: Green Button Connect My Data
The ability to authorize a third party to automatically retrieve EUI from a utility via Web Services.

## Slide 6: Green Button Connect My Data
The ability to authorize a third party to automatically retrieve EUI from a utility via Web Services.

## Slide 7: Download/Connect My Data and the Utility Enterprise
MDMA
Has EUI
Billing System
Has Cost
Web Portal
Green Button Data W/O Cost
Green Button Data W/ Cost
GUI Web Interface
RESTful Web Services
Utility Enterprise
Web
Green Button Download My Data
Green Button Connect My Data
Edge
MDMA = Meter Data Management Agent
EUI = Energy Usage Information

## Slide 8: Energy Data Jam  Rate Integration
This Green Button “Rate Integration” effort was launched by NIST and its partners based on an idea generated at the July Energy Data Jam (http://www.whitehouse.gov/blog/2012/07/12/open-data-clean-secure-energy-future, led by US CTO Todd Park, OSTP).
Project successful in addressing the current challenge to providing cost-attributed Energy Usage Information by encouraging third party services and apps.
Demonstration by example of concept using existing schema fragments from industry standards (ZigBee and NAESB) and sample Green Button data generated by the Green Button Software Development Kit.

## Slide 9: The Tariff Demo
A tariff is created based on the tariff.xsd schema.
A sample Green Button Data file is selected which does not have cost data in it.
A simple batch file is executed that applies the XSLT (xml style sheet) to process the no-cost Green Button Data File into
one that has costs
Green Button Data XML File – No Costs
Green Button Data XML File – With Costs
XSLT w/jscript
Block and Tier Tariff XML File
espi. xsd
tariff.xsd
1
2
3
4

## Slide 10: The Tariff Demo
Green Button Data XML File – No Costs
Green Button Data XML File – With Costs
XSLT w/jscript
Block and Tier Tariff XML File
espi.xsd
tariff.xsd
1
2
3
4
Tariff created
Green Button file without costs selected
Batch file applies the XSLT (xml style sheet)
Producing modified Green Button file with costs

## Slide 11: Summary
A Tariff Schema was assembled
A sample Tariff.xml instance file created based on California “block and tier” concept
XSLT created to transform non-cost-containing Green Button Data to cost-containing Green Button Data
Potential future work: your input and discussions on the attractiveness of this concept may lead to the creation of a new Priority Action Plan proposal to produce a standard Tariff XML Schema

## Slide 12: Additional Details

## Slide 13: Sample Block and Tier Tariff
Description | Local Time | Tier | Block | start value (kWh) | Price
Off Peak | 00:00-08:00 | 1 | 1 | 0 | $ 0.22
 |  |  | 2 | 150 | $ 0.24
 |  |  | 3 | 250 | $ 0.33
 |  |  | 4 | 300 | $ 0.37
 |  |  | 5 | 350 | $ 0.40
Mid Peak | 8:00-10:00 | 2 | 1 | 0 | $ 0.32
 |  |  | 2 | 150 | $ 0.34
 |  |  | 3 | 250 | $ 0.43
 |  |  | 4 | 300 | $ 0.47
 |  |  | 5 | 350 | $ 0.50
On Peak | 10:00-18:00 | 3 | 1 | 0 | $ 0.52
 |  |  | 2 | 150 | $ 0.54
 |  |  | 3 | 250 | $ 0.73
 |  |  | 4 | 300 | $ 0.77
 |  |  | 5 | 350 | $ 0.80
Mid Peak | 18:00-24:00 | 2 | 1 | 0 | $ 0.32
 |  |  | 2 | 150 | $ 0.34
 |  |  | 3 | 250 | $ 0.43
 |  |  | 4 | 300 | $ 0.47
 |  |  | 5 | 350 | $ 0.50

## Slide 14: Tariff Schema

## Slide 15: SGIP PAP20: Green Button ESPI Evolution Roadmap Going Forward …
Standards (NAESB)
International Version
T&C (UCAIug)
Implementation (EnergyOS)
REQ.18/WEQ.19 Maintenance Update
ESPI Errata Update
REQ.21/REQ.22
ESPI New Reqs Update
Green Button Download My Data Test Plan
Green Button Connect My Data Test Plan
Green Button SDK
OpenESPI
UCAIug ITCA
Specification Deliverables:
SGIP PAP Activities:
Requirements for Green Button and ESPI Rollout
Facilitate/Coordinate SGIP interactions
Privacy assurance recommendations
Cybersecurity recommendations for EUI exchanges
CSWG
Test plan consistency
ITCA assurances
SGTCC
Coordinates with
PAP 20
Requirements for standards and test criteria
Education on implementation strategies, standards, use cases and test criteria
SGIMC

## Slide 16: Alternate paths to EUI – single format
Acknowledgements to graphics owners
Single Data Format: all at once
Single Data Format: as sequence
Sources of EUI
Uses of EUI
Via: ESPI, SEP2, Web Portal
Power Utility

## Slide 17: Web Technologies for Definition and Presentation of EUI File Format
X
XML Schema (XSD)
XML
XSLT
Describes the rules of file format
Contains customer EUI data in standard file format and references to XSD and XSLT
Defines how to transform for humans
Standard EUI file Format

## Slide 18: Technical and Organizational Links
Smart Grid Interoperability Panel (SGIP)
SGIP PAP20 Green Button ESPI evolution: http://collaborate.nist.gov/twiki-sggrid/bin/view/SmartGrid/GreenButtonESPIEvolution
SGIP Green Button Initiative TWiki: https://collaborate.nist.gov/twiki-sggrid/bin/view/SmartGrid/GreenButtonInitiative
SGIP Green Button FAQ: https://collaborate.nist.gov/twiki-sggrid/bin/view/SmartGrid/GreenButtonFAQ
Standards:
NAESB PAP10 Task Force Project Page : http://www.naesb.org/smart_grid_pap10.asp
NAESB ESPI Task Force Project Page : http://www.naesb.org/espi_task_force.asp
NAESB ESPI and PAP10 email lists: to subscribe contact Denise Rager at NAESB - drager@naesb.org
NAESB Green Button Portal - http://www.naesb.org/ESPI_Standards.asp
Users Group:
UCAIug OpenADE Task Force Home Page: http://osgug.ucaiug.org/sgsystems/OpenADE/default.aspx
UCAIug OpenADE Mail List: http://www.smartgridlistserv.org/cgi/wa.exe?A0=OPENSG-OPENADE
UCAIug OpenADE Meetings: tuesdays at 3:00 EST - https://www2.gotomeeting.com/join/844935738, 415-363-0070 #844-935-738
UCAIug OpenADE Green Button Issues List: http://osgug.ucaiug.org/HelpDesk/Lists/servicerequests/GreenButton.aspx
Open Source Implementations and tools:
EnergyOS OpenESPI Mail List: http://groups.google.com/group/energyos_espi/subscribe?hl=en
EnergyOS OpenESPI Web Site: http://www.openespi.org/
EnergyOS OpenESPI Meetings: mondays at 12:00 EST - https://www2.gotomeeting.com/join/129392235, +1 (516) 453-0010 #129-392-235
EnergyOS OpenESPI GitHub: https://github.com/energyos/OpenESPI
EnergyOS OpenESPI GitHub Issues List: https://github.com/energyos/OpenESPI/issues
General OpenESPI information: https://github.com/energyos/OpenESPI/wiki/
Energy OS home page: http://energyos.org/
Other:
NREL OpenEnergyInfo Green Button Apps Repository: http://en.openei.org/wiki/Main_Page
Green Button Data Sample/Developmental Web Site: http://www.greenbuttondata.org

## Slide 19: Questions?
Marty Burns | David Wollman | Erich Gunther
Hypertek, Inc. | NIST | EnerNex
marty@hypertek.us | david.wollman@nist.gov | erich@enernex.com